## Slide 1: Using a Portable Fire Extinguisher Utilizing the PASS Method

## Slide 2: Types of Fires
Class A – Class A – Ordinary combustibles such as wood, paper, plastic, rubber and cloth
Class B – Flammable and combustible liquids and gases
Class C – Electrical fires (in electrical equipment)
Class D – Combustible metals
Class K – Cooking oils (commercial kitchens)

## Slide 3: Safety Rules
Use an extinguishers ONLY if you have been trained to uses it.
Fire Extinguishers are for SMALL FIRES in the early stages
Know where you extinguishers are located

## Slide 4: Safety Rules cont.
Do not put extinguishers in an upright position unless you are holding it
All fire extinguishers should have an inspection tag and trigger seal and a pin
After use Do Not place back into serviced until it has been refilled.

## Slide 5: Fire Extinguisher Anatomy

## Slide 6: Extinguishing a Fire with an Extinguisher
Locate the fire
Stand 6 to 8 feet away from fire
Stand in an upright position holding the extinguisher firmly with both hands
Proper Position

## Slide 7: Extinguishing a Fire with PASS Method
Pull the Pin – Pull the pin breaking the thin wire or plastic seal
Aim the nozzle – Aim the nozzle or hose towards the base of the fire
Squeeze the handle – Squeeze the handle together to release the agent
Sweep the nozzle – Sweep the nozzle back and forth to cover the burning material

## Slide 8: Extinguishing a Fire with PASS Method

## Slide 9: Using a Portable Fire Extinguisher Utilizing the PASS Method
Any Questions?